## Slide 1: High Performing Cache Hierarchies for Server Workloads
Aamer Jaleel*, Joseph Nuzman, Adrian Moga,
Simon Steely Jr., Joel Emer*
Intel Corporation, VSSAD
( *Now at NVIDIA )
International Symposium on High Performance Computer Architecture (HPCA-2015)
Notes: Thank you for the introduction. Good morning. This work was done while I was at the VSSAD research group at Intel.
In this talk I will show that the existing strategy of using the same core for client and server processors results in the same type of cache hierarchies for client and server workloads. However, such a strategy leaves performance on the table for commercial server workloads. This talk presents an overview of a high performing cache hierarchy that performs well for both client and server workloads.

## Slide 2: Motivation
  Factors making caching important
    CPU speed >> Memory speed
    Chip Multi-Processors (CMPs)
  Variety of Workload Segments:
    Multimedia, games, workstation, commercial server, HPC, …
  High Performing Cache Hierarchy:
    Reduce main memory accesses ( e.g. RRIP replacement policy )
    Service on-chip cache hits with low latency
iL1
dL1
L2
iL1
dL1
L2
LLC
Bank
LLC
Bank
iL1
dL1
L2
LLC
Bank
Notes: A mature field such as caching still has significant importance today! This is because the memory speeds continue to lag behind processor speeds. Additionally, the multi-core era coupled by the wide variety of workload segments poses significant challenges on designing better cache hierarchies.
In general, a high performing cache hierarchy has two properties. First, it reduces accesses to main memory. Our group has done on designing high performing low overhead replacement policies such as RRIP that are implemented in Intel processors today.
Second, a high performing cache hierarchy must service on-chip cache hits with low latency. Unfortunately, while our existing strategy does a good job at reducing accesses to memory, it is unable to provide low on-chip hit latency, especially for commercial workloads.

## Slide 3: LLC Hits SLOW in Conventional CMPs
INTERCONNECT
CORE 0
32KB L1
256KB L2
2MB L3 “slice”
+ 3 cycs
+ 10 cycs
+ 14 cycs
+ 10 cycs
Typical Xeon Hierarchy
CORE 1
32KB L1
256KB L2
2MB L3 “slice”
CORE 2
32KB L1
256KB L2
2MB L3 “slice”
CORE3
32KB L1
256KB L2
2MB L3 “slice”
CORE ‘n’
32KB L1
256KB L2
2MB L3 “slice”
  Large on-chip shared LLC  more application working-set resides on-chip
  LLC access latency increases due to interconnect  LLC hits become slow
L2 Hit Latency: ~15 cycles LLC Hit Latency: ~40 cycles
Notes: To illustrate this problem, let me first provide with you a background on the existing Xeon multi-core three-level cache hierarchy. A typical Xeon core consists of 32KB L1 I/D caches and a 256KB L2 cache and a 2MB L3 bank attached to it. A CMP consists of many cores and L3 banks. The L3 cache is typically shared by all cores on-chip. This enables a gigantic LLC that allows more of the application working set to reside on chip.
Since the LLC is shared, an interconnect path is needed to access the appropriate slice. The consequence however is that the LLC access latency increases, and LLC hits become slow.
To give you an idea, the individual latencies are provided on the right. As can be seen, the interconnect and LLC bank access latency amounts to more than 50% of the LLC hit latency

## Slide 4: Performance Characterization of Workloads
Chart: Total Execution Time
| SPEC CPU2006 | SERVER
compute | 0.7746 | 0.62416
L2-cache | 0.030725 | 0.086906
L3-cache | 0.073192 | 0.14144
Memory | 0.12148 | 0.14749
Chart: Total Execution Time
| SPEC CPU2006 | SERVER
compute | 0.83208 | 0.69484
L2-cache | 0.039542 | 0.12739
L3-cache | 0.05487 | 0.10066
Memory | 0.073508 | 0.07711
Prefetching OFF
Prefetching ON
Server Workloads Spend Significant Execution Time Waiting on L3 Cache Access Latency 
Single-Thread Simulated on 16-core CMP
15-40%
10-30%

## Slide 5: Performance Inefficiencies in Existing Cache Hierarchy
  Problem: L2 cache ineffective when the frequently referenced application working set is larger than L2 (but fits in LLC)
  Solution: Increase L2 Cache Size
LLC
iL1
L2
dL1
Must also increase LLC size for
an inclusive cache hierarchy
iL1
L2
dL1
LLC
LLC
NOT SCALABLE
LLC
iL1
L2
dL1
LLC
iL1
L2
dL1
Redistribute cache resources
Requires reorganizing hierarchy
SCALABLE

## Slide 6: Cache Organization Studies
iL1
256KB L2
2MB LLC
dL1
(Inclusive LLC)
iL1
512KB L2
1.5 MB LLC
dL1
(Exclusive LLC)
iL1
1MB L2
1MB LLC
dL1
(Exclusive LLC)
OR
  Increase L2 cache size while reducing LLC  Design exclusive cache hierarchy
    Exclusive hierarchy helps retain existing on-chip caching capacity ( i.e. 2MB / core )
    Exclusive hierarchy enables better average cache access latency
    Access latency overhead for larger L2 cache is minimal (+0 for 512KB, +1 cycle for 1MB)

## Slide 7: Performance Sensitivity to L2 Cache Size
Chart: Performance Relative to Baseline
| dh | games | multimedia | office | productivity | server | SPEC CPU2006 | workstation | ALL
512KB L2 /1.5MB L3 (Exclusive) | 1.0031 | 1.0083 | 1.0075 | 1.0155 | 1.0108 | 1.0286 | 1.0052 | 1.0061 | 1.0085
1MB L2 /1MB L3 (Exclusive) | 1.0043 | 1.0121 | 1.0121 | 1.0267 | 1.0173 | 1.0506 | 1.0108 | 1.0121 | 1.015
Server Workloads Observe the MOST Benefit from Increasing L2 Cache Size

## Slide 8: Server Workload Performance Sensitivity to L2 Cache Size
Where Is This Performance Coming From????
A Number of Server Workloads Observe > 5% benefit from larger L2 caches
Chart: Performance Relative to Baseline
| mgs | tpch | gidx | ibuy | ncpr | ncps | sap | sas | sjap | sjbb | sweb | tpcc | ALL
256K-I | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1
512KB L2 /1.5MB L3 (Exclusive) | 1.0343 | 1.0028 | 1.0006 | 1.0443 | 1.0246 | 1.0109 | 1.0436 | 1.0028 | 1.0473 | 1.0386 | 1.0211 | 1.0744 | 1.0286
1MB L2 /1MB L3 (Exclusive) | 1.049 | 1.0019 | 1.0006 | 1.0976 | 1.0425 | 1.0105 | 1.0804 | 1.003 | 1.1053 | 1.0684 | 1.0312 | 1.1273 | 1.0506

## Slide 9: Understanding Reasons for Performance Upside
  Larger L2  Lower L2 miss rate  More requests serviced at L2 hit latency
  Two types of requests: Code Requests and Data Requests
    Which requests serviced at L2 latency provide bulk of performance?
  Sensitivity Study: In baseline inclusive hierarchy (256KB L2), evaluate:
    i-Ideal: L3 code hits always serviced at L2 hit latency
    d-Ideal: L3 data hits always serviced at L2 hit latency
    id-Ideal: L3 code and data hits always serviced at L2 hit latency
    NOTE: This is NOT a perfect L2 study.
Notes:     This study still fills code and data into the L2. The sensitivity study also takes into account latency due to misses to memory. The study measures latency sensitivity for only those requests that hit in the L3.

## Slide 10: Code/Data Request Sensitivity to Latency
Performance of Larger L2 Primarily From Servicing Code Requests at L2 Hit Latency
(Shouldn’t Be Surprising – Server Workloads Generally Have Large Code Footprints)
Chart: Performance Relative to Baseline
| mgs | tpch | gidx | ibuy | ncpr | ncps | sap | sas | sjap | sjbb | sweb | tpcc | ALL
i-Ideal | 1.0366 | 1.0031 | 1.0011 | 1.159 | 1.0321 | 1.0048 | 1.1142 | 1 | 1.1388 | 1.0496 | 1.0431 | 1.1478 | 1.0593
d-Ideal | 1.0254 | 1.0024 | 1.0013 | 1.0154 | 1.0525 | 1.01 | 1.0227 | 1.0034 | 1.0144 | 1.1093 | 1.0116 | 1.0418 | 1.0254
id-Ideal | 1.0588 | 1.0053 | 1.0023 | 1.169 | 1.0735 | 1.012 | 1.1311 | 1.0034 | 1.1513 | 1.1566 | 1.0506 | 1.1737 | 1.0802
1MB L2 / 1MB L3 (Exclusive) | 1.049 | 1.0019 | 1.0006 | 1.0976 | 1.0425 | 1.0105 | 1.0804 | 1.003 | 1.1053 | 1.0684 | 1.0312 | 1.1273 | 1.0506
256KB L2 /2MB L3 (Inclusive)
sensitive to code
sensitive to data

## Slide 11
MPKI
MPKI
Cache Size (MB)
Cache Size (MB)
MPKI
MPKI
Cache Size (MB)
Cache Size (MB)
SERVER
LARGE
CODE
WORKING
SET
(0.5MB – 1MB)

## Slide 12: Enhancing L2 Cache Performance for Server Workloads
  Observation: Server workloads require servicing code requests at low latency
    Avoid processor front-end from frequent “hiccups” to feed the processor back-end
    How about prioritize code lines in the L2 cache using the RRIP replacement policy
  Proposal: Code Line Preservation (CLIP) in L2 Caches
    Modify L2 cache replacement policy to preserve more code lines over data lines
0
Imme-
diate
1
Inter-
mediate
2
far
3
distant
eviction
re-reference
re-reference
re-reference
No Victim
No Victim
No Victim
data re-reference
data re-reference
data re-reference
data inserts
inserts
code inserts

## Slide 13: Performance of Code Line Preservation (CLIP)
Still Recommend Larger L2 Cache Size and Exclusive Cache Hierarchy for Server Workloads
Chart: Performance Relative to Baseline
| mgs | tpch | gidx | ibuy | ncpr | ncps | sap | sas | sjap | sjbb | sweb | tpcc | ALL
256KB L2 / 2MB L3 (Inclusive+CLIP) | 1.0078 | 0.99414 | 1 | 1.0627 | 1 | 0.99138 | 1.0364 | 1 | 1.074 | 1.0345 | 1.002 | 1.0802 | 1.0231
512KB L2 / 1.5MB L3 (Exclusive) | 1.0343 | 1.0028 | 1.0006 | 1.0443 | 1.0246 | 1.0109 | 1.0436 | 1.0028 | 1.0473 | 1.0386 | 1.0211 | 1.0744 | 1.0286
512KB L2 / 1.5MB L3 (Exclusive+CLIP) | 1.0152 | 0.99629 | 1.0005 | 1.1102 | 1.0232 | 1.0006 | 1.0651 | 1.0016 | 1.1063 | 1.0494 | 1.0215 | 1.1096 | 1.0407
1MB L2 / 1MB L3 (Exclusive) | 1.049 | 1.0019 | 1.0006 | 1.0976 | 1.0425 | 1.0105 | 1.0804 | 1.003 | 1.1053 | 1.0684 | 1.0312 | 1.1273 | 1.0506
1MB L2 / 1MB L3 (Exclusive+CLIP) | 1.0225 | 0.99683 | 1.0003 | 1.1413 | 1.0404 | 1.0042 | 1.0803 | 1.0017 | 1.1161 | 1.0781 | 1.0372 | 1.1184 | 1.052
CLIP similar
to doubling L2 cache

## Slide 14: Tradeoffs of Increasing L2 Size and Exclusive Hierarchy
  Functionally breaks recent replacement policies (e.g. RRIP)
    Solution: save re-reference information in L2 (see paper for details)

## Slide 15: Call For Action: Open Problems in Exclusive Hierarchies
  Functionally breaks recent replacement policies (e.g. RRIP)
    Solution: save re-reference information in L2 (see paper for details)
  Effective caching capacity of the cache hierarchy reduces
2MB
iL1
256KB L2
dL1
2MB
iL1
256KB L2
dL1
2MB
iL1
256KB L2
dL1
2MB
iL1
256KB L2
dL1
1MB
iL1
1MB L2
dL1
1MB
iL1
1MB L2
dL1
1MB
iL1
1MB L2
dL1
1MB
iL1
1MB L2
dL1

## Slide 16: Call For Action: Open Problems in Exclusive Hierarchies
  Functionally breaks recent replacement policies (e.g. RRIP)
    Solution: save re-reference information in L2 (see paper for details)
  Effective caching capacity of the cache hierarchy reduces
2MB
iL1
256KB L2
dL1
2MB
iL1
256KB L2
dL1
2MB
iL1
256KB L2
dL1
2MB
iL1
256KB L2
dL1
1MB
iL1
1MB L2
dL1
1MB
iL1
1MB L2
dL1
1MB
iL1
1MB L2
dL1
1MB
iL1
1MB L2
dL1
iL1
256KB L2
dL1
2MB
iL1
256KB L2
dL1
2MB
iL1
256KB L2
dL1
2MB
iL1
256KB L2
dL1
iL1
1MB L2
dL1
1MB
iL1
1MB L2
dL1
1MB
iL1
1MB L2
dL1
iL1
1MB L2
dL1
8MB
4MB

## Slide 17: Call For Action: Open Problems in Exclusive Hierarchies
  Functionally breaks recent replacement policies (e.g. RRIP)
    Solution: save re-reference information in L2 (see paper for details)
  Effective caching capacity of the cache hierarchy reduces
iL1
256KB L2
dL1
2MB
iL1
256KB L2
dL1
2MB
iL1
256KB L2
dL1
2MB
iL1
256KB L2
dL1
iL1
1MB L2
dL1
1MB
iL1
1MB L2
dL1
1MB
iL1
1MB L2
dL1
iL1
1MB L2
dL1
8MB
4MB
Private Large L2 Caches Unusable by Active Cores When CMP is Under-subscribed
IDLE
IDLE
IDLE
IDLE
  Idle Cores  Waste of Private L2 Cache Resources
  e.g. two cores active with combined working set size greater than 4MB but less than 8MB
Revisit Existing Mechanisms on Private/Shared Cache Capacity Management

## Slide 18: Call For Action: Open Problems in Exclusive Hierarchies
  Functionally breaks recent replacement policies (e.g. RRIP)
    Solution: save re-reference information in L2 (see paper for details)
  Effective caching capacity of the cache hierarchy reduces
iL1
256KB L2
dL1
2MB
iL1
256KB L2
dL1
2MB
iL1
256KB L2
dL1
2MB
iL1
256KB L2
dL1
8MB
Shared Data Replication in L2 caches Reduces Hierarchy Capacity
  Large Shared Data Working Set  Effective Hierarchy Capacity Reduces

## Slide 19: Call For Action: Open Problems in Exclusive Hierarchies
  Functionally breaks recent replacement policies (e.g. RRIP)
    Solution: save re-reference information in L2 (see paper for details)
  Effective caching capacity of the cache hierarchy reduces
iL1
256KB L2
dL1
2MB
iL1
256KB L2
dL1
2MB
iL1
256KB L2
dL1
2MB
iL1
256KB L2
dL1
iL1
1MB L2
dL1
1MB
iL1
1MB L2
dL1
1MB
iL1
1MB L2
dL1
iL1
1MB L2
dL1
8MB
4MB
Shared Data Replication in L2 caches Reduces Hierarchy Capacity
Revisit Existing Mechanisms on Private/Shared Cache Data Replication
  Large Shared Data Working Set  Effective Hierarchy Capacity Reduces
  e.g. 0.5MB shared data, exclusive hierarchy capacity reduces by ~25% (0.5MB*5=2.25MB replication)

## Slide 20: Multi-Core Performance of Exclusive Cache Hierarchy
Call For Action: Develop Mechanisms to Recoup Performance Loss
16T-server 1T, 2T,4T, 8T, and 16T SPEC workloads

## Slide 21: Summary
  Problem: On-chip hit latency is a problem for server workloads
  We show: server workloads have large code footprints that need to be serviced out of L1/L2 (not L3)
  Proposal: Reorganize Cache Hierarchy to Improve Hit Latency
    Inclusive hierarchy with small L2  Exclusive hierarchy with large L2
    Exclusive hierarchy enables improving average cache access latency

## Slide 22
Q&A

## Slide 24: High Level CMP and Cache Hierarchy Overview
  CMP consists of several “nodes” connected via an on-chip network
    A typical “node” consists of a “core” and “uncore”
      “core”  CPU, L1, and L2 cache
      “uncore”  L3 cache slice, directory, etc.
iL1
unified L2
L3 “slice”
dL1
“core”
“uncore”
“ring”
“mesh”

## Slide 25: Performance of Code Line Preservation (CLIP)
On Average, CLIP Performs Similar to Doubling Size of the Baseline Cache
It is Still Better to Increase L2 Cache Size and Design Exclusive Cache Hierarchy
Chart: Performance Relative to Baseline
| mgs | tpch | gidx | ibuy | ncpr | ncps | sap | sas | sjap | sjbb | sweb | tpcc | ALL
256KB L2 / 2MB L3 (Inclusive+CLIP) | 1.0078 | 0.99414 | 1 | 1.0627 | 1 | 0.99138 | 1.0364 | 1 | 1.074 | 1.0345 | 1.002 | 1.0802 | 1.0231
512KB L2 / 1.5MB L3 (Exclusive) | 1.0343 | 1.0028 | 1.0006 | 1.0443 | 1.0246 | 1.0109 | 1.0436 | 1.0028 | 1.0473 | 1.0386 | 1.0211 | 1.0744 | 1.0286
512KB L2 / 1.5MB L3 (Exclusive+CLIP) | 1.0152 | 0.99629 | 1.0005 | 1.1102 | 1.0232 | 1.0006 | 1.0651 | 1.0016 | 1.1063 | 1.0494 | 1.0215 | 1.1096 | 1.0407
1MB L2 / 1MB L3 (Exclusive) | 1.049 | 1.0019 | 1.0006 | 1.0976 | 1.0425 | 1.0105 | 1.0804 | 1.003 | 1.1053 | 1.0684 | 1.0312 | 1.1273 | 1.0506
1MB L2 / 1MB L3 (Exclusive+CLIP) | 1.0225 | 0.99683 | 1.0003 | 1.1413 | 1.0404 | 1.0042 | 1.0803 | 1.0017 | 1.1161 | 1.0781 | 1.0372 | 1.1184 | 1.052
CLIP similar
to doubling L2 cache

## Slide 26: Performance Characterization of Workloads
Server Workloads Spend Significant Fraction of Time Waiting for LLC Latency

## Slide 28: LLC Latency Problem with Conventional Hierarchy
CORE
  Fast Processor + Slow Memory  Cache Hierarchy
  Multi-level Cache Hierarchy:
    L1 Cache: Designed for high bandwidth
    L2 Cache: Designed for latency
    L3 Cache: Designed for capacity
32KB L1
256KB L2
2MB L3 “slice”
~ 4 cycs
~12 cycs
~40 cycs
~200 cycs
DRAM
*L3 Latency includes network latency
~10 cycs
network
Typical Xeon Hierarchy
Increasing Cores  Longer Network Latency
 Longer LLC Access Latency 
Notes: Transition from MEM-CPI to LLC-CPI is missing

## Slide 29: Performance Inefficiencies in Existing Cache Hierarchy
  Problem: L2 cache ineffective at hiding latency when the frequently referenced application working set is larger than L2 (but fits in LLC)
  Solution1: Hardware Prefetching
    Server workloads tend to be “prefetch unfriendly”
    State-of-the-art prefetching techniques for server workloads too complex
  Solution2: Increase L2 Cache Size
    Option 1: If inclusive hierarchy, must increase LLC size as well 
      Limited by how much on-chip die area can be devoted to cache space
    Option 2: Re-organize the existing cache hierarchy
      Decide how much area budget to spend on each cache level in the hierarchy
OUR FOCUS

## Slide 30: Code/Data Request Sensitivity to Latency
Performance of Larger L2 Primarily From Servicing Code Requests at L2 Hit Latency
(Shouldn’t Be Surprising – Server Workloads Generally Have Large Code Footprints)
Chart: Performance Relative to Baseline
| mgs | tpch | gidx | ibuy | ncpr | ncps | sap | sas | sjap | sjbb | sweb | tpcc | ALL
i-Ideal | 1.0366 | 1.0031 | 1.0011 | 1.159 | 1.0321 | 1.0048 | 1.1142 | 1 | 1.1388 | 1.0496 | 1.0431 | 1.1478 | 1.0593
d-Ideal | 1.0254 | 1.0024 | 1.0013 | 1.0154 | 1.0525 | 1.01 | 1.0227 | 1.0034 | 1.0144 | 1.1093 | 1.0116 | 1.0418 | 1.0254
id-Ideal | 1.0588 | 1.0053 | 1.0023 | 1.169 | 1.0735 | 1.012 | 1.1311 | 1.0034 | 1.1513 | 1.1566 | 1.0506 | 1.1737 | 1.0802
1MB L2 / 1MB L3 (Exclusive) | 1.049 | 1.0019 | 1.0006 | 1.0976 | 1.0425 | 1.0105 | 1.0804 | 1.003 | 1.1053 | 1.0684 | 1.0312 | 1.1273 | 1.0506
256KB L2 /2MB L3 (Inclusive)
sensitive to code
sensitive to data

## Slide 31: Cache Hierarchy 101: Multi-level Basics
  Fast Processor + Slow Memory  Cache Hierarchy
  Multi-level Cache Hierarchy:
    L1 Cache: Designed for bandwidth
    L2 Cache: Designed for latency
    L3 Cache: Designed for capacity
L1
L2
LLC
DRAM

## Slide 32: L2 Cache Misses